## Slide 1
YieldMindX
AI-Based Correlation Engine for EOL Yield Optimization
Project summary -- Stage 1 (Yield Prediction) and Stage 2 (Relationship Discovery & Validation)
Notes: Welcome / framing slide. State the two-part goal up front: (1) predict End-Of-Line sorting yield accurately, and (2) discover and statistically validate WHICH process/ET parameters and combinations actually drive that yield. Everything in this deck traces back to those two goals.

## Slide 2
BACKGROUND
Project Motivation
2/15
▪ EOL (End-Of-Line) SortingYield is only known at the very end of the production flow -- long after the process/ET (electrical test) steps that actually determined it.
▪ Hundreds of process and electrical-test parameters are recorded per wafer, but only a small subset genuinely drives yield.
▪ Today, engineers search for root causes largely by manual correlation review and domain intuition -- slow, and easy to miss real multi-parameter (2-way / 3-way) interactions.
▪ Business need: an automated, statistically defensible system that (a) predicts yield early and (b) tells engineers WHICH knobs and combinations matter, with a process window / threshold they can act on.
1,500
wafers in the dataset
100 x 15
lots x wafers/lot
~1,400
raw process/ET columns
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: The core pain point: yield is a LATE, lagging signal. By the time SortingYield is measured, the wafer has already been through the full process. If we can predict yield early AND explain which parameters/combinations drive it, engineers can intervene upstream instead of discovering problems at the very end.

## Slide 3
OVERVIEW
System Goal
3/15
STAGE 1
Yield Prediction Engine
Predict SortingYield as accurately and reliably as possible from leakage-free process/ET predictors, using grouped, leakage-safe validation.
STAGE 2
Relationship Discovery & Validation Engine
Discover and statistically VALIDATE which single parameters, pairs, and triples of parameters actually explain yield behavior -- with shapes, thresholds, and confidence levels engineers can act on.
Stage 1 answers "what will the yield be?" Stage 2 answers "why -- and which knobs, thresholds, and combinations actually matter?" Both stages share the same leakage-safe, LotName-grouped validation discipline.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Two-part system. Stage 1 is a closed, conventional supervised-learning problem: predict a continuous target. Stage 2 is the harder, more novel part: move beyond prediction toward causally-suggestive, statistically validated relationship discovery -- single-parameter shapes, 2-way interactions, 3-way interactions -- each with a confidence label.

## Slide 4
DATA
Data Overview
4/15
1,500
wafers
100 x 15
lots x wafers/lot
~1,430
raw CSV columns
1,425
Stage 2 predictor universe
SortingYield
prediction target
▪ Target: SortingYield (continuous, %).
▪ Original predictors: raw process and electrical-test (ET) parameters recorded per wafer -- 1,405 numeric + 20 one-hot-encoded categorical (VendorName, Technology, MaskSetName, etc.) = 1,425 predictors, after leakage/ID/duplicate columns are removed.
▪ 307 project-created ENGINEERED features (stage-range/std/delta features built from raw ET columns) exist but are EXCLUDED from the current official Stage 1 and Stage 2 analysis, so every result in this deck is based on original, physically-meaningful raw measurements only.
▪ Grouping: every wafer belongs to exactly one of 100 lots (15 wafers/lot) -- all validation is grouped by LotName so no lot's wafers ever span both train and test/validation.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Emphasize the exclusion of the 307 engineered features from the CURRENT official numbers -- this was a deliberate methodology choice to keep the headline results interpretable in terms of raw, physically meaningful measurements; the engineered features remain available for a future checkpoint if needed. Also stress LotName grouping -- it's the backbone of every validation number in this deck.

## Slide 5
DATA QUALITY
Data Leakage and Feature Eligibility
5/15
Some raw columns are other yield roll-ups or values statistically/deterministically derived from the outcome itself -- using them as predictors would let the model "cheat." These are excluded from BOTH stages.
Excluded column | Why it's leakage
Actual Sorting Yield (%) | r = 0.99 with target -- same underlying metric
TotalYield | r = 0.92 with target -- rollup that includes it
EstimatedSupplyChipsCount | Derived ratio bakes in the yield outcome (r = 0.92)
LineYield / BackEndYield / VIYield / LTYield | Separate downstream yield-stage outputs
▪ Also excluded: metadata/ID/traceability columns (LotName, WaferNum, dates) -- kept only as grouping keys, never as predictors.
▪ Exact-duplicate columns (e.g. MaskSetName_group, a 1:1 duplicate of MaskSetName) are removed.
▪ Every exclusion is justified from evidence found directly in the data (correlation, duplication, derived-ratio checks) -- not from the synthetic ground-truth document, which is deliberately kept out of the discovery pipeline.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This slide answers the inevitable question 'why isn't column X in the model?' Every exclusion here is evidence-based (correlation coefficients, exact duplication, or a derived-ratio check) -- verifiable directly from the raw CSV, not assumed.

## Slide 6
STAGE 1
Stage 1 Pipeline -- Yield Prediction Engine
6/15
Raw data (1,430 cols)
Leakage & ID removal
Original predictors only (1,425)
Feature selection / ranking
Model comparison
Final model (ElasticNet)
▪ Every step respects LotName grouping -- no wafer's lot-mates ever leak across train/validation/holdout.
▪ The 307 engineered features are excluded from this pipeline; feature selection ranks only the 1,425 original raw predictors.
▪ Three model families were compared fairly on the same predictor set and the same splits before selecting a final model (next slide).
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Walk left to right. This is a conventional, disciplined supervised-learning pipeline -- the novelty in this project is less the pipeline shape and more the rigor applied at every step (leakage-safe, grouped, engineered-features-excluded, fairly-compared).

## Slide 7
STAGE 1
Stage 1 Models and Metrics
7/15
Model | CV RMSE | CV MAE | CV R² | Holdout RMSE | Holdout R²
ElasticNet | 0.189 | 0.150 | 0.9927 | 0.170 | 0.9943
LightGBM | 0.220 | 0.140 | 0.9901 | 0.178 | 0.9937
Random Forest | 0.350 | 0.253 | 0.9756 | 0.234 | 0.9891
Metric formulas
R² = 1 − SS_res / SS_tot RMSE = sqrt( mean( (y_true − y_pred)² ) ) MAE = mean( |y_true − y_pred| )
▪ 5-fold grouped cross-validation (by LotName) -- mean across folds.
▪ Untouched holdout set, evaluated once at the end.
▪ Repeated-holdout stability: ElasticNet had the tightest spread across repeats (RMSE std = 0.008 vs. 0.016-0.018 for the tree models).
▪ Target-shuffle negative control: SortingYield randomly permuted, same pipeline re-run.
▪ All three models' shuffled R² collapsed far below their real R² -- no leakage detected.
▪ ElasticNet's shuffled R² (-0.002) was the CLEANEST/closest-to-zero of the three.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: RMSE/MAE/R2 are the standard regression metrics (formulas recap on a later slide). The headline: ElasticNet -- a comparatively simple, LINEAR model -- outperforms both tree-based models here, is the most stable across repeated holdouts, and shows the cleanest collapse under target shuffling. This is a meaningful, evidence-based result, not a default choice.

## Slide 8
STAGE 1
Stage 1 Result -- Considered Closed
8/15
✓
Strong prediction
Holdout R² = 0.994, RMSE = 0.17 yield points -- essentially production-grade accuracy.
✓
Stable performance
Lowest variance across 5 repeated grouped holdouts of any model tested.
✓
Clean target-shuffle
Shuffled-target R² collapses to ~0 (-0.002) -- confirms no leakage, genuine signal.
✓
ElasticNet selected
Best CV/holdout accuracy AND best stability AND cleanest shuffle behavior -- a consistent winner across every criterion, not just raw RMSE.
Conclusion: Stage 1 is CLOSED. No further prediction-model work is planned for Stage 1.
Notes: Stage 1 is done. Four independent lines of evidence (accuracy, stability, shuffle-test, and consistent model selection) all point the same direction. This closure is what freed up the project to invest fully in the harder Stage 2 relationship-discovery problem.

## Slide 9
STAGE 2
Stage 2 Pipeline -- Relationship Discovery
9/15
Run B feature universe (1,425 preds)
LightGBM (global model)
Spline / GAM (single-param)
Cross-stage analysis
Explicit 2-way / 3-way interaction testing
Candidate generation V1 -> V5
Relationship Validation Engine (FDR + permutation)
▪ "Run B" = the locked Stage 2 predictor universe: original raw process/ET predictors only, zero engineered features, same leakage exclusions as Stage 1.
▪ Each stage ADDS a complementary lens on the data -- none replaces the previous one; all outputs from every version (V1-V5, MLP, EBM, Relationship Validation Engine) remain frozen and available.
▪ The whole pipeline was built and iteratively improved WITHOUT reading the synthetic ground-truth answer key -- it is used only afterward, for validation.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This is the map for the rest of the deck. Two rows: top row is the 'characterize what a single model already knows' phase; bottom row is the 'explicitly go looking for interactions and statistically prove them' phase, culminating in the newest component, the Relationship Validation Engine.

## Slide 10
CONCEPT
Why Prediction Is Not Enough
10/15
A model that predicts yield accurately does not, by itself, tell an engineer WHICH parameter to adjust, by how much, or which combinations matter.
Question | Formula (simple form)
Predict yield from all predictors | Y ≈ f(X)
Does parameter A alone explain yield? | Y ≈ f(A)
Do A and B act independently (additive)? | Y ≈ f(A) + f(B)
Do A and B interact (joint, non-additive)? | Y ≈ f(A, B)
Is there a genuine 3-way effect (A, B, C)? | compare: main effects + pairwise vs. + full 3-way term
Interaction-strength formulas
2-way gain = performance[f(A,B)] − performance[f(A)+f(B)] 3-way gain = performance[main+pairwise+3-way] − performance[main+pairwise]
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This slide is the conceptual pivot of the whole deck. Prediction (Y~f(X)) answers 'what will happen.' Everything below it is about answering 'why' in an explicit, testable way -- and each row is a genuinely different, formally-tested hypothesis, not just a looser version of the same thing.

## Slide 11
STAGE 2
Stage 2 Methods Used
11/15
Method | Role | Status
LightGBM | Global nonlinear model; SHAP/gain/permutation importance; base for interaction tests | Trusted, in use
Spline / GAM | Model-free single-parameter shape (thresholds, U-shapes, process windows) | Trusted, in use
Explicit 2-way / 3-way testing | Additive-vs-joint and lower-order-vs-full grouped-CV comparisons | Trusted, in use
Permutation / FDR validation | Genuine statistical significance testing (Relationship Validation Engine) | Trusted, in use
MLP (small neural net) | Tested as a complementary relationship detector | Rejected -- see below
EBM (Explainable Boosting Machine) | Tested as a complementary interpretable interaction detector | Rejected -- see below
MLP and EBM were tested but NOT accepted as trusted relationship detectors:
▪ MLP: overall predictive signal was real (clean shuffle collapse), but its single-feature "importance" evidence did NOT separate from noise under its own negative control (86% of features looked "strong" even on a shuffled target).
▪ EBM: main effects were clean and well-calibrated, but its automatic pairwise-interaction selection failed its own negative control (shuffled-target interactions scored ~190x HIGHER than the real ones) -- all 15 EBM-selected interactions were labeled inconclusive.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Important credibility point: we did not just try methods that worked and hide the ones that didn't. MLP and EBM were both tried in good faith as complementary relationship detectors, both were rigorously negative-control-tested exactly like every other method, and both failed that test for interaction detection specifically -- so they are explicitly excluded from the trusted evidence base. This is a feature of the project's rigor, not a gap.

## Slide 12
STAGE 2
Stage 2 Validation Metrics
12/15
▪ Ground-truth recovery classification (used only in dedicated, after-the-fact validation checkpoints, never during discovery):
– EXACT / APPROXIMATE / PARTIAL / MISSED / NOT GENERATED
▪ Grouped-fold stability: does the finding reproduce across independent LotName-grouped folds (e.g. improved in 5/5 or 4/5 folds)?
▪ Negative control / target shuffle: does the finding's evidence collapse when SortingYield is randomly shuffled? (It must, or the method isn't trustworthy.)
▪ Benjamini-Hochberg FDR: controls the expected proportion of false discoveries among everything called "significant," across thousands of simultaneous tests.
▪ Incremental R²: how much additional variance a joint/full model explains beyond the additive/lower-order model -- the core interaction-strength metric.
▪ Delta RMSE / delta MAE: the accuracy improvement (or lack of it) from adding an interaction term, under grouped cross-validation.
▪ Coverage: explicitly distinguishes NOT SCREENED / SCREENED BUT NOT PROMOTED / PROMOTED BUT NOT CONFIRMED / CONFIRMED, so "we didn't test it" is never confused with "we tested it and found nothing."
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This is the vocabulary the rest of the results slides rely on. The two ideas worth emphasizing to a non-ML audience: (1) negative controls -- we deliberately try to fool the method with randomized data and require it to fail; (2) FDR -- with thousands of simultaneous tests, some 'discoveries' are expected by pure chance, and FDR is the formal accounting for that.

## Slide 13
STAGE 2
Current Stage 2 Results
13/15
3 / 9
Exactly found
4 / 9 (44.4%)
Exact + Approximate
7 / 9 (77.8%)
Partial-or-better
(Measured against a synthetic ground-truth benchmark of 9 planted relationships, used ONLY for after-the-fact validation.)
Remaining problem: interaction candidate generation / coverage
▪ Every relationship this system actually got a chance to test has produced at least a partial, reproducible finding -- zero outright "missed" among testable cases.
▪ The 2 remaining untested relationships have ALL of their component pieces independently confirmed real; the gap is that no candidate-generation pass (across 5 successive versions) has yet combined them into the exact tested pair/triple.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Frame this honestly: the system is not missing signal, it is missing COVERAGE for two specific, already-partially-confirmed relationships. This distinction (confirmation power vs. candidate generation) is the single most important diagnostic conclusion of the whole Stage 2 effort so far, and it directly motivates the Relationship Validation Engine on the next slide.

## Slide 14
STAGE 2 -- NEWEST COMPONENT
Relationship Validation Engine
14/15
A new, complementary component whose job is to directly and STATISTICALLY validate relationships -- not just discover candidates. Independently audited and improved since first built.
Single-feature validation (baseline vs nonlinear)
2-way: ADD vs JOINT
3-way: lower-order vs full
Permutation empirical p-values
Benjamini- Hochberg FDR
Family | Hypotheses tested | Survive FDR (q≤0.05)
Single-parameter | 1,405 | 1,048 (74.6%)
2-way interactions | 11,920 | 11,622 (97.5%)
3-way interactions | 11,002 | 9,635 (87.6%)
▪ Every LotName-grouped fold used for stability, not just accuracy.
▪ Negative control (real vs. shuffled-target rate) PASSES cleanly for all three families.
▪ Independently audited: fixed a permutation-shuffle methodology gap and a dormant threshold bug -- conclusions held, calibration still PASSES.
Candidate-generation coverage improvements (2 rounds, ground-truth-free)
▪ Per-feature guaranteed candidate slots + evidence-ranked (not random) triple chaining: pair feature-coverage 80%->91%, triple feature-coverage 43%->72%.
▪ Shrunk (de-noised) interaction score, reusing the same statistical shrinkage principle as the validator itself: measurably better agreement with confirmed results; calibration still PASSES.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This is the newest, most statistically rigorous layer of Stage 2. Unlike every earlier checkpoint, it computes genuine empirical p-values (from real permutation testing, not approximations) and applies formal FDR control. It has since been independently audited (one methodology gap found and fixed, conclusions unchanged) and improved twice on purely generic, ground-truth-free grounds -- candidate coverage is measurably broader and the interaction score is measurably less noisy, while calibration keeps passing cleanly.

## Slide 15
WRAP-UP
Current Status and Next Steps
15/15
Stage 1
CLOSED -- production-grade accuracy, validated, no further prediction-model work planned.
Stage 2
STILL UNDER DEVELOPMENT -- validation engine audited and improved twice; a few specific combinations remain unresolved.
Progress since the audit was proposed
Methodology audit (COMPLETE -- 1 gap fixed, PASSED)
Candidate-generation fix (COMPLETE -- coverage improved)
Interaction-score fix (COMPLETE -- less noisy)
Ground truth re-checked twice (unchanged, honest)
Remaining gap is now precisely diagnosed: the last few relationships involve real, individually-confirmed features whose COMBINED effect is smaller than hundreds of other real interactions in this data -- a relative-ranking issue, not a broken test.
Final goal
A validated engineering relationship report -- process knobs, thresholds and process windows, confirmed interactions, and actionable Golden Routes (condition sets associated with high yield) and Worsen Routes (condition sets associated with low yield) -- delivered with an explicit statistical confidence level for every claim.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Close on the roadmap, not just the status. Stage 1 is done. Since the Relationship Validation Engine was first built, it has been independently audited (passed, one gap fixed), and its candidate generation and interaction scoring were each improved on purely generic, ground-truth-free grounds -- coverage and score quality both measurably improved, calibration kept passing throughout. Ground truth was rechecked twice after these fixes: the numbers held steady, and the remaining gap is now understood precisely as a relative-effect-size ranking issue among many real interactions, not a detection failure. The end deliverable is not a model -- it's an actionable engineering report engineers can use directly on the line.