## Slide 1
Boaz Kalderon
Yulia Kucher
Linoy Halifa
Notes: Welcome / framing slide. State the two-part goal up front: (1) predict End-Of-Line sorting yield accurately, and (2) discover and statistically validate WHICH process/ET parameters and combinations actually drive that yield. Everything in this deck traces back to those two goals.

## Slide 2
OVERVIEW
System Goal
3/15
STAGE 1
Yield Prediction Engine
Predict SortingYield as accurately and reliably as possible from leakage-free process/ET predictors, using grouped, leakage-safe validation.
STAGE 2
Relationship Discovery & Validation Engine
Discover and statistically VALIDATE which single parameters, pairs, and triples of parameters actually explain yield behavior -- with shapes, thresholds, and confidence levels engineers can act on.
Stage 1 answers "what will the yield be?" Stage 2 answers "why -- and which knobs, thresholds, and combinations actually matter?" Both stages share the same leakage-safe, LotName-grouped validation discipline.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Two-part system. Stage 1 is a closed, conventional supervised-learning problem: predict a continuous target. Stage 2 is the harder, more novel part: move beyond prediction toward causally-suggestive, statistically validated relationship discovery -- single-parameter shapes, 2-way interactions, 3-way interactions -- each with a confidence label.

## Slide 3
DATA QUALITY
Data Leakage and Feature Eligibility
5/15
Some raw columns are other yield roll-ups or values statistically/deterministically derived from the outcome itself -- using them as predictors would let the model "cheat." These are excluded from BOTH stages.
Excluded column | Why it's leakage
Actual Sorting Yield (%) | r = 0.99 with target -- same underlying metric
TotalYield | r = 0.92 with target -- rollup that includes it
EstimatedSupplyChipsCount | Derived ratio bakes in the yield outcome (r = 0.92)
LineYield / BackEndYield / VIYield / LTYield | Separate downstream yield-stage outputs
▪ Also excluded: metadata/ID/traceability columns (LotName, WaferNum, dates) -- kept only as grouping keys, never as predictors.
▪ Exact-duplicate columns (e.g. MaskSetName_group, a 1:1 duplicate of MaskSetName) are removed.
▪ Every exclusion is justified from evidence found directly in the data (correlation, duplication, derived-ratio checks) -- not from the synthetic ground-truth document, which is deliberately kept out of the discovery pipeline.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This slide answers the inevitable question 'why isn't column X in the model?' Every exclusion here is evidence-based (correlation coefficients, exact duplication, or a derived-ratio check) -- verifiable directly from the raw CSV, not assumed.

## Slide 4
STAGE 1
Stage 1 Pipeline -- Yield Prediction Engine
6/15
Raw data (1,430 cols)
Leakage & ID removal
Original predictors only (1,425)
Feature selection / ranking
Model comparison
Final model (ElasticNet)
▪ Every step respects LotName grouping -- no wafer's lot-mates ever leak across train/validation/holdout.
▪ The 307 engineered features are excluded from this pipeline; feature selection ranks only the 1,425 original raw predictors.
▪ Three model families were compared fairly on the same predictor set and the same splits before selecting a final model (next slide).
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Walk left to right. This is a conventional, disciplined supervised-learning pipeline -- the novelty in this project is less the pipeline shape and more the rigor applied at every step (leakage-safe, grouped, engineered-features-excluded, fairly-compared).

## Slide 5
STAGE 1
Stage 1 Models and Metrics
7/15
Model | CV RMSE | CV MAE | CV R² | Holdout RMSE | Holdout R²
ElasticNet | 0.189 | 0.150 | 0.9927 | 0.170 | 0.9943
LightGBM | 0.220 | 0.140 | 0.9901 | 0.178 | 0.9937
Random Forest | 0.350 | 0.253 | 0.9756 | 0.234 | 0.9891
Metric formulas
R² = 1 − SS_res / SS_tot RMSE = sqrt( mean( (y_true − y_pred)² ) ) MAE = mean( |y_true − y_pred| )
▪ 5-fold grouped cross-validation (by LotName) -- mean across folds.
▪ Untouched holdout set, evaluated once at the end.
▪ Repeated-holdout stability: ElasticNet had the tightest spread across repeats (RMSE std = 0.008 vs. 0.016-0.018 for the tree models).
▪ Target-shuffle negative control: SortingYield randomly permuted, same pipeline re-run.
▪ All three models' shuffled R² collapsed far below their real R² -- no leakage detected.
▪ ElasticNet's shuffled R² (-0.002) was the CLEANEST/closest-to-zero of the three.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: RMSE/MAE/R2 are the standard regression metrics (formulas recap on a later slide). The headline: ElasticNet -- a comparatively simple, LINEAR model -- outperforms both tree-based models here, is the most stable across repeated holdouts, and shows the cleanest collapse under target shuffling. This is a meaningful, evidence-based result, not a default choice.

## Slide 6
STAGE 2
Stage 2 Pipeline -- Relationship Discovery
9/15
Run B feature universe (1,425 preds)
LightGBM (global model)
Spline / GAM (single-param)
Cross-stage analysis
Explicit 2-way / 3-way interaction testing
Candidate generation V1 -> V5
Relationship Validation Engine (FDR + permutation)
▪ "Run B" = the locked Stage 2 predictor universe: original raw process/ET predictors only, zero engineered features, same leakage exclusions as Stage 1.
▪ Each stage ADDS a complementary lens on the data -- none replaces the previous one; all outputs from every version (V1-V5, MLP, EBM, Relationship Validation Engine) remain frozen and available.
▪ The whole pipeline was built and iteratively improved WITHOUT reading the synthetic ground-truth answer key -- it is used only afterward, for validation.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This is the map for the rest of the deck. Two rows: top row is the 'characterize what a single model already knows' phase; bottom row is the 'explicitly go looking for interactions and statistically prove them' phase, culminating in the newest component, the Relationship Validation Engine.

## Slide 7
STAGE 2
Stage 2 Methods Used
11/15
Method | Role | Status
LightGBM | Global nonlinear model; SHAP/gain/permutation importance; base for interaction tests | Trusted, in use
Spline / GAM | Model-free single-parameter shape (thresholds, U-shapes, process windows) | Trusted, in use
Explicit 2-way / 3-way testing | Additive-vs-joint and lower-order-vs-full grouped-CV comparisons | Trusted, in use
Permutation / FDR validation | Genuine statistical significance testing (Relationship Validation Engine) | Trusted, in use
MLP (small neural net) | Tested as a complementary relationship detector | Rejected -- see below
EBM (Explainable Boosting Machine) | Tested as a complementary interpretable interaction detector | Rejected -- see below
MLP and EBM were tested but NOT accepted as trusted relationship detectors:
▪ MLP: overall predictive signal was real (clean shuffle collapse), but its single-feature "importance" evidence did NOT separate from noise under its own negative control (86% of features looked "strong" even on a shuffled target).
▪ EBM: main effects were clean and well-calibrated, but its automatic pairwise-interaction selection failed its own negative control (shuffled-target interactions scored ~190x HIGHER than the real ones) -- all 15 EBM-selected interactions were labeled inconclusive.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Important credibility point: we did not just try methods that worked and hide the ones that didn't. MLP and EBM were both tried in good faith as complementary relationship detectors, both were rigorously negative-control-tested exactly like every other method, and both failed that test for interaction detection specifically -- so they are explicitly excluded from the trusted evidence base. This is a feature of the project's rigor, not a gap.

## Slide 8
STAGE 2
Stage 2 Validation Metrics
12/15
▪ Ground-truth recovery classification (used only in dedicated, after-the-fact validation checkpoints, never during discovery):
– EXACT / APPROXIMATE / PARTIAL / MISSED / NOT GENERATED
▪ Grouped-fold stability: does the finding reproduce across independent LotName-grouped folds (e.g. improved in 5/5 or 4/5 folds)?
▪ Negative control / target shuffle: does the finding's evidence collapse when SortingYield is randomly shuffled? (It must, or the method isn't trustworthy.)
▪ Benjamini-Hochberg FDR: controls the expected proportion of false discoveries among everything called "significant," across thousands of simultaneous tests.
▪ Incremental R²: how much additional variance a joint/full model explains beyond the additive/lower-order model -- the core interaction-strength metric.
▪ Delta RMSE / delta MAE: the accuracy improvement (or lack of it) from adding an interaction term, under grouped cross-validation.
▪ Coverage: explicitly distinguishes NOT SCREENED / SCREENED BUT NOT PROMOTED / PROMOTED BUT NOT CONFIRMED / CONFIRMED, so "we didn't test it" is never confused with "we tested it and found nothing."
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This is the vocabulary the rest of the results slides rely on. The two ideas worth emphasizing to a non-ML audience: (1) negative controls -- we deliberately try to fool the method with randomized data and require it to fail; (2) FDR -- with thousands of simultaneous tests, some 'discoveries' are expected by pure chance, and FDR is the formal accounting for that.

## Slide 9
STAGE 2 -- NEWEST COMPONENT
Relationship Validation Engine
14/15
A new, complementary component whose job is to directly and STATISTICALLY validate relationships -- not just discover candidates.
Single-feature validation (baseline vs nonlinear)
2-way: ADD vs JOINT
3-way: lower-order vs full
Permutation empirical p-values
Benjamini- Hochberg FDR
Family | Hypotheses tested | Survive FDR (q≤0.05)
Single-parameter | 1,405 | 1,109 (78.9%)
2-way interactions | 6,677 | 6,591 (98.7%)
3-way interactions | 13,064 | 12,265 (93.9%)
▪ Every LotName-grouped fold is used for stability, not just accuracy.
▪ Negative control: real-target discovery rate vs. shuffled-target rate, checked for ALL three families.
▪ Calibration gate: PASS across all three families -- shuffled-target findings collapsed to 2-6% of the real rate.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: This is the newest, most statistically rigorous layer of Stage 2. Unlike every earlier checkpoint, it computes genuine empirical p-values (from real permutation testing, not approximations) and applies formal FDR control. It passed its own calibration gate cleanly on all three relationship families -- this is a meaningfully stronger evidence bar than anything used earlier in the project.

## Slide 10
WRAP-UP
Current Status and Next Steps
15/15
Stage 1
CLOSED -- production-grade accuracy, validated, no further prediction-model work planned.
Stage 2
STILL UNDER DEVELOPMENT -- discovery and confirmation methods are mature; coverage of a few specific combinations remains open.
Next steps
Methodology audit of the Relationship Validation Engine
If audit passes: ground-truth validation
Final goal
A validated engineering relationship report -- process knobs, thresholds and process windows, confirmed interactions, and actionable Golden Routes (condition sets associated with high yield) and Worsen Routes (condition sets associated with low yield) -- delivered with an explicit statistical confidence level for every claim.
YieldMindX -- AI-Based Correlation Engine for EOL Yield Optimization
Notes: Close on the roadmap, not just the status. Stage 1 is done. Stage 2's discovery/validation machinery is mature and has passed its own calibration checks; the next gate is an independent methodology audit of the newest engine, and only after that passes does the project move to ground-truth validation. The end deliverable is not a model -- it's an actionable engineering report engineers can use directly on the line.